## Slide 1
Module 1: Essentials for roof construction, maintenance, renovation & demolition
Funded by the European Union. Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Education and Culture Executive Agency (EACEA). Neither the European Union nor EACEA can be held responsible for them.
Open licence: This document is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International licence.

## Slide 2
  Learning Unit 1: Building regulations & standards
04

## Slide 3
03
Green roofs reduce reflected noise by up to 3 dB and improve sound insulation by up to 8 dB. These advantages are particularly useful for buildings located e.g. under an air corridor
or hosting premises with high noise sources (e.g. discos).
A green roof can retain 50-90 % of rainfall, relieving the load on sewerage systems.
A large part of this water evaporates, while the rest drains from the roof with some delay.
The capacity of pipes, drains and rainwater tanks can be reduced
Green roofs cool and humidify the surrounding air, making a valuable contribution to improving the microclimate in city centres. Due to less overheating, air conditioners also work more economically.
Due to the large vegetated area and the slowing down of air currents, green roofs filter out 10-20 % of dust.
Nitrates and other components of air and rainwater are also absorbed and utilised.
Natural light
O2
H O2
CO2
Improves the microclimate
Absorbs dust and harmful substances
Retains water
Improves sound insulation
Green roofs, and especially species-rich extensive green roofs, return green spaces to the environment that are often sacrificed for the construction of buildings.
Green roofs improve the thermal insulation of the roof. Green roofs with officially recognised thermal insulation coefficients can add value to the energy balance.
Green roofs can be used for a variety of purposes: as a simple protected natural area, as a relaxing garden, barbecue area, play area or for sports activities.
The green cover effectively protects the waterproofing membrane from UV radiation, hail, heat and cold.
Stress (expansion) due to temperature fluctuations is eliminated, thus increasing the life of the waterproofing layer
cold
hot
Reduces energy costs
Prolongs the life of the roof
It offers a natural habitat
Create new spaces
Why a green roof?
In addition to its aesthetic appeal, a green roof provides undeniable ecological and economic benefits, provided it is built correctly!

## Slide 4
  Learning Unit 1: Building regulations & standards
05-07
05
EUROPEAN LEGISLATION
Directive 2002/91/EC = energy performance of buildings.
Directive 2010/31/EU = 'nearly zero-energy' building.
Directive 2012/27/EU = building renovation strategy.
COM(2013) 249 = Green Infrastructure - Strengthening Natural Capital in Europe.
Directive 2018/844/EU = New Energy Efficiency in Buildings Directive.

## Slide 5
  Learning Unit 1: Building regulations & standards
06
COM(2013) 249 final 'Green Infrastructure.
EUROPEAN INITIATIVES
Directive (EU) 2018/844 'New Energy Efficiency Directive'.
"Green roofs and walls to insulate and/or shade buildings, reduce energy demand for heating and cooling, and contribute to European targets against greenhouse gas emissions and in favour of decarbonisation".
Covenant of Mayors of 2008 (The Covenant of Mayors) and the Global Covenant of Mayors for Climate and Energy of 2017, aimed at supporting all actions to accelerate the decarbonisation of EU territories.
05-07

## Slide 6
  Learning Unit 2: Roofing tools & equipment
08

## Slide 7
  Learning Unit 2: Roofing tools & equipment
09-15
09
Extensive green roof
Intensive green roofs can easily be compared to building a Dachgarten on a roof. They are usually multifunctional and usable. They weigh more and their structure is deeper.
Maintenance must be regular and depends on the layout, as well as the plants chosen. Depending on the thickness of the substrate, any solution is possible: lawn, perennials, shrubs, trees and other options such as ponds, basins, pergolas and terraces.
Types of green roofs
Extensive green roofs
Low-maintenance vegetative structure instead of a layer of gravel
Minimum maintenance
No additional irrigation required
From a combination of moss and Sedum to one of grass and herbs
Thickness 8-20 cm
Weight 60-250 kg/m2
Simple intensive green roofs
Setting up a vegetative structure for higher demands
Average maintenance
Periodic irrigation
From combining grass and herbs to planting shrubs
Thickness 12-25 cm
Weight 150-300 kg/m2
Intensive green roofs
Setting up gardens on usable flat roofs
High maintenance
Regular irrigation
From lawn or perennials to shrubs and trees
Thickness 15-200 cm
Weight 200-3000 kg/m2
There are two basic types of green roofs: extensive and intensive, with many variations in layout and stratigraphy (simple intensive green roofs).
Intensive green roof
Extensive green roofs are an environmentally friendly alternative to conventional surface protection such as gravel. They are lightweight and their thickness is reduced. For this type of system, we use proven plant communities adapted to the environmental conditions (sun, wind, humidity, etc.) prevailing on the roof in question. Once implemented, the extensive green roof requires very little care. As a rule, maintenance is limited to one or two operations per year.

## Slide 8
  Learning Unit 2: Roofing tools & equipment
10
Types of green roofs
On the adequately cleaned and wet roof slab, a sloping screed (1÷5%) will be made, well adhered and smoothed with a trowel, consisting of a concrete prepared with 200÷250 kg of cement per m3 of mixture; for areas where a thickness of less than 3 cm is envisaged, the screed will be made from a mortar prepared with 350 kg of cement per m3 of sand.
The screed may consist of concrete with light mineral granules prepared with 250 kg of cement per m3 of mixture.
The sloping screed may also consist of cellular concrete or concrete lightened with non-mineral granules as long as it is sufficiently cohesive to permit membrane adhesion.
On roofs consisting of prefabricated reinforced concrete panels, 20 cm wide strips of waterproofing membrane will be torch-bonded across the tile approach lines, either before laying the sloping screed or, in the case of a waterproofing membrane or vapour barrier, laid directly onto the prefabricated panel.
The laying surface must be smooth and flat.
A concrete surface is defined as such if under a 2 metre straightedge resting in all directions no differences in level of more than 10 mm appear, and under a 0.20 metre straightedge, differences of more than 3 mm appear.
The surface must be trowelled, free of cracks or depressions, which will be sealed with mortar.
Roughness and all residues from site work such as nails, sheet metal, wood, etc. must be removed.
Before application, the laying surface must be clean and dry. For cement and hollow-core concrete laying surfaces, a drying period of 8 days to 3 weeks should be allowed, depending on the season.
Application in total adherence
The torching of the roll compound must affect both the membrane and the substrate at the same time, with the roll predominating. The burner flame should also be directed at the already laid membrane, which will be affected by the overlapping.
LAYING PLAN
The vertical parts of the roof garden must also be waterproofed.
First, all reliefs must be painted with bituminous adhesion primer.
The perimeter wall will be covered with a layer of waterproofing membrane that will be turned up at least 10 cm on the flat side.
The waterproof covering will be made of the same membrane that will later be applied as the first layer, taking care to match the heads of the sheets to the previous flap made.
The second layer will be made of a root-resistant waterproofing membrane, the sheets will be unrolled parallel to the first one and straddle its overlaps and will be torch-bonded to it.
The sheets will be laid up to the foot of the relief, which will then be covered by the sheet of the same nature that will be turned up to the surface by at least 20 cm.
Vertical waterproofing shall exceed
15 to 20 cm above ground level and must be protected as indicated below.
INTENSIVE GREEN ROOF
Protective plastic film
AREAS TO BE FLAMED
bitumen waterproofing membranes
Preparation
of the laying surface
Vertical parts
Methods for connecting the membrane to the laying surface
09-15

## Slide 9
  Learning Unit 2: Roofing tools & equipment
11
INSTALLATION DETAILS AND WARNINGS
INTENSIVE GREEN ROOF
Vertical parts
Conformation of the roof garden near vertical parts
Gardens larger than 100 m2. A sterile area at least 40 cm wide will be provided near the vertical parts of the roof at the flap of the waterproof covering, which can be created in accordance with the two examples shown below.
In the first example, the height reached by the lap of the waterproof covering on the vertical parts will be at least 15 cm higher than the ground level.
Gardens with a surface area of less than 100 m2 . In the vicinity of the vertical parts of the roof in correspondence with the turn-up of the waterproof covering, the sterile zone can be created by draining polystyrene panels at least 3.5 cm thick or by a composite draining and filtering geotextile at least 2 cm thick under load.
Also in this case, the height reached by the lap of the waterproof covering on the vertical parts will be at least 15 cm higher than the ground level.
Cultivated land
0.15 m min
Root-proofing system
Layer
filter
Cultivated land
Root-proofing system
Removable plate
Filter layer
Cultivated land
Filter layer
Root-proofing system
Draining polystyrene panels
09-15

## Slide 10
  Learning Unit 2: Roofing tools & equipment
12
INSTALLATION DETAILS AND WARNINGS
INTENSIVE GREEN ROOF
Exhausts
Exhaust outlets can be made of lead, copper or synthetic materials; in all cases, it is necessary that the connection crown and the diameter of the outlet are amply dimensioned.
The crown of the nozzle will be closed between the two layers of the waterproofing membrane, which are flame-welded.
To avoid inconveniences, it is advisable that
drains are easy to inspect, so a sump fitted with a removable plate must be built around the drain.
The sump rests on the protected mantle
at that point with a layer of flame-bonded bitumen waterproofing membranes. For small roof gardens, it is possible to replace the sump with a mound of expanded clay placed above the drain and almost as high as the entire thickness of the layers.
Conformation of the roof garden near the drains
No plant species with woody stems may be planted around drains for a distance of at least 40 cm.
Root-proofing system
Removable plate
Filter layer
Exhausts
In the vicinity of the joint, it is advisable to raise two walls higher than the layer of topsoil and to protect them in the same way as for reliefs.
To avoid the formation of condensation, the joint should be filled with compressible insulating material. Flat joints are to be avoided at all costs.
Conformation of the roof garden near expansion joints
Buried joints.
As with drains at a distance of at least 40 cm from both sides of the expansion joints, no plant species with woody stems may be planted.
Visible joints.
At the raised joints bordered by walls, the same procedure as for the vertical parts will be followed, providing a sterile zone consisting of polystyrene draining panels at least 3.5 cm thick or a composite draining and filtering geotextile at least 2 cm thick under load.
Removable plate
Root-proofing system
Compressible insulation material
Filter layer
Filter layer
Removable plate
Root-proofing system
Compressible insulation material
09-15

## Slide 11
  Learning Unit 2: Roofing tools & equipment
13
INSTALLATION DETAILS AND WARNINGS
INTENSIVE GREEN ROOF
Embankments
Tree pits
If a terrace roof is partly buried or in contact with an embankment, in addition to the normal waterproofing, a strip of protective plastic film must be laid around the perimeter of the roof in contact with the ground, with a vertical waterproofing lap of at least one metre.
Root-proof waterproofing membrane
In the case of gardening work of a certain degree of commitment, where the planting of stem plants of a certain height is envisaged, pots of sufficient size and height must be provided, which will provide deep burying for normal root growth.
These tanks will be placed on the drainage layer, having
taken care to separate them with a weight-distributing layer.
The tank itself will have a drainage layer inside with drains and a separating filter.
Filter
Draining layer
Filter layer
Spreader layer
09-15

## Slide 12
  Learning Unit 2: Roofing tools & equipment
14
INSTALLATION DETAILS AND WARNINGS
EXTENSIVE GREEN ROOF
Extensive green roofing in the vicinity of the drain
Extensive green roof conformation in proximity
of a rainwater collection channel
  1. Support
  2. Vapour barrier
  3. Thermal insulation
  6. Cultivated land
  7. Discharge
  5. Root-proof waterproofing membrane
  4. Waterproofing membrane
  1. Support
  2. Vapour barrier
  3. Thermal insulation
  6. Cultivated land
  7. Rainwater collection channel
  8. Draining metal element
  5. Root-proofing membrane
  4. Waterproofing membrane
09-15

## Slide 13
  Learning Unit 2: Roofing tools & equipment
15
INSTALLATION DETAILS AND WARNINGS
EXTENSIVE GREEN ROOF
Example of an extensive green roof on a slope
  1. Support
  2. Vapour barrier
  3. Thermal insulation
  6. Cultivated land
  5. Root-proofing membrane
  4. Waterproofing membrane
  1. Support
09-15

## Slide 14
  Learning Unit 3: Roof assemblies & structures
16

## Slide 15
  Learning Unit 3: Roof assemblies & structures
17-28
18
Double-layer ventilated roof (cold roof)
Vegetation
Vegetation layer
protection/division/storage area
root-resistant waterproofing
protection zone and division
Planking
counter-ordering of ventilation battens
rafters
planking
vapour pressure compensation layers
vapour barrier

## Slide 16
  Learning Unit 3: Roof assemblies & structures
17-28
19
Roofs with little slope on structure
wooden
Areas of implementation
  roof 'Pult'
    low-energy houses
    passive houses
  pitched roofs
    with very long beams
    with simple roof shapes

## Slide 17
  Learning Unit 3: Roof assemblies & structures
17-28
20
Single-layer roof -
without thermal insulation
Vegetation
layer of vegetation
protection/division/storage area
root-resistant waterproofing
compensation layer
e.g. rough concrete roofing

## Slide 18
  Learning Unit 3: Roof assemblies & structures
17-28
21
Single-layer roof with thermal insulation
(warm roof)
Vegetation
layer of vegetation
protection/division/storage area
root-resistant waterproofing
division area
thermal insulation
vapour barrier
compensation layer
supporting substructure

## Slide 19
  Learning Unit 3: Roof assemblies & structures
22
Single-layer roof - with thermal insulation (inverted roof)
vegetation
layer of vegetation
filter/drainage and ventilation
thermal insulation (XPS-G)
root-resistant waterproofing
division and compensation layer
rough concrete roofing
17-28

## Slide 20
  Learning Unit 3: Roof assemblies & structures
23
Thermal insulation for single-layer roof - inverted roof
In intensive winterization, attention must be paid to the tightness of the thermal insulation
A vapour expansion layer (ventilation layer) must be placed above the thermal insulation
17-28

## Slide 21
  Learning Unit 3: Roof assemblies & structures
24
Scale roofs
The building techniques and scale roofing materials currently used are not suitable for greening.
So brick roofs are not indicated
Sheet metal roofs are only suitable in certain cases with additional precautions
17-28

## Slide 22
  Learning Unit 3: Roof assemblies & structures
25
Green roof checklist
The following points absolutely must be checked before the roof is built:
STATIC
PENDENCE
PROTECTION AGAINST ROOT PENETRATION
ROOF EDGES/WALLS
ROOF DRAINAGE
LOCATION
17-28

## Slide 23
  Learning Unit 3: Roof assemblies & structures
26
Statics
Load analysis
  The maximum water storage capacity of the structure with all its layers must be calculated.
Wind suction capacity
  Calculations must be performed on the structure and all its layers in a dry condition.
17-28

## Slide 24
  Learning Unit 3: Roof assemblies & structures
27
Weight of a green roof
To be considered:
Weight of the entire green roof (saturated with water)
Snow load
Wind suction capacity
Load from use
Approximate rule: approx. 15 kg / m² per cm construction layer
Flat roofs must be made with a
minimum slope of 1.8 % !
17-28

## Slide 25
  Learning Unit 4: Ventilation and water drainage systems
29

## Slide 26
  Learning Unit 4: Ventilation and water drainage systems
30-43
30
Important construction details
Drainage
  basis for calculation: maximum rainwater supply of 300 l/ha.s.
  calculation : Q = q . j . F
    Q = quantity of water to be disposed of in litres
    q = calculation of rainwater supply (see above)
    j = runoff coefficient
    F = greened roof surface
  j for intensive greening= 0.2
  j for 8 cm extensive greening = 0.3
  j for extensive greening under 8 cm = 0.5

## Slide 27
  Learning Unit 4: Ventilation and water drainage systems
34
Functional layers
Greening
Vegetation substrate
Filter layer
Water storage element
Protection layer
(separation and anti-friction coating)
30-43

## Slide 28
  Learning Unit 4: Ventilation and water drainage systems
35
Example 1 of construction of the
extensive layer
Draining mat
Protection, drainage and filtration layer
Suitable for inverted roofs
30-43

## Slide 29
  Learning Unit 4: Ventilation and water drainage systems
36
Example 2 of construction of the
extensive layer
Accumulation and drainage components
For example in HD-PE plastic material
Suitable for inverted roofs
Continuous laying under slabs and green surfaces is possible
Additional water storage element
30-43

## Slide 30
  Learning Unit 4: Ventilation and water drainage systems
39
Extensive - one-layer construction
Trade-off between economy and greening result
For greening large industrial surfaces
For small areas (private)
For limited needs
30-43

## Slide 31
  Learning Unit 4: Ventilation and water drainage systems
40
Example of layered construction,
sloping roof 5 - 15°
The water storage element balances surface drainage
The filter layer is missing
The anti-cutting substrate is filled directly
Continuous waterproofing, no sliding waves in the surface
30-43

## Slide 32
  Learning Unit 4: Ventilation and water drainage systems
41
Extensive greening of pitched roofs Roof slope 15 - 25°
Additional anti-cutting system with slatted frame
Only necessary until roots have formed in the substrate
30-43

## Slide 33
  Learning Unit 4: Ventilation and water drainage systems
42
Example 1 of intensive layered construction
With water storage element
Large element thickness for optimisation of 'local water storage'.
Bubbles on the underside for drainage purposes
Optimal growing conditions
30-43

## Slide 34
  Learning Unit 4: Ventilation and water drainage systems
43
Example 2 intensive layered construction
With drainage and storage elements
Pressure resistance requires stronger materials
Can be used as a 'lost' coating
"Optimal 'buildability' as a requirement
30-43

## Slide 35
  Learning Unit 5: Installation and maintenance practices for roofs
44

## Slide 36
  Learning Unit 5: Installation and maintenance practices for roofs
45-57
45
Why roofs with substrates?
water storage and disposal
accumulation and turnover of substances
volume of voids
stability of the structure
weight
mineral-based
organic aggregates

## Slide 37
  Learning Unit 5: Installation and maintenance practices for roofs
47
Extensive greening methods
Sowing by hand
Planting with low bushes
Mats with pre-cultivated vegetation
Wet willy
45-57

## Slide 38
  Learning Unit 5: Installation and maintenance practices for roofs
49
The spray mass
Protects seed and shoots from drying out
It ensures that the seed and shoots bind well with the growing medium
Activates soil vitality
Ensures slow and regular release of nutrients
Increases water storage capacity
Protects against erosion
45-57

## Slide 39
  Learning Unit 5: Installation and maintenance practices for roofs
53
Pre-grown mats
Sedum mats (grasses) pre-cultivated on a degradable biological substrate e.g. coconut fibre
For extensive greening of flat roofs with a slope of up to approx. 15°.
45-57

## Slide 40
  Learning Unit 5: Installation and maintenance practices for roofs
55
Start-up maintenance (growth)
In extensive greening:
  It serves firstly to achieve the desired crop form (adequate vegetation development)
  60% floor coverage
  75% of the described sedum cuttings have grown
  90% of the described plants have grown
  75% coverage by cultivation mats
  Uniform structure, rooted, etc.
45-57

## Slide 41
  Learning Unit 5: Installation and maintenance practices for roofs
57
Maintenance for growth
and maintenance
Maintenance for growth takes place after adequate vegetation development until handover to the client
Maintenance for upkeep begins after delivery to the client.
Isolated interventions may be required :
Drainage system checks
Delivery of nutrients
Pruning or grubbing up woody formations
New sowing for large areas where no greening has taken place
Cleaning of cast iron strips from foliage and wild vegetation
45-57

## Slide 42
  Learning Unit 6: Dismantling/demolition
58

## Slide 43
  Learning Unit 6: IDismantling/demolition
59-67
59
Demolition techniques
It is very important to plan the sequence of works in advance based on a thorough knowledge of the structures and working techniques of the time of construction. There are no demolition techniques that are certainly always and in all cases valid.
The demolition technique must be studied on a case-by-case basis and adapted (even as the work progresses) to the needs and state of the work being carried out.

## Slide 44
  Learning Unit 6: IDismantling/demolition
60
Strengthening of structures
Before work begins, the structure to be demolished is analysed and verified:
location of the work (urban, industrial, suburban context, etc.)
intended use (civil dwelling, industrial shed, school building, etc.)
the type of construction and the era to which it dates
construction materials
verification of the conservation and stability conditions of the various structures to be demolished.
Depending on the result of this verification, the necessary reinforcement and shoring works must be carried out to prevent untimely collapses during demolition.
59-67

## Slide 45
  Learning Unit 6: IDismantling/demolition
61
Structure analysis
In the analysis of the structure conducted beforehand, it is necessary:
distinguish load-bearing parts from accessory parts,
be aware of any damage or alteration that structures or materials have suffered as a result of:
different loads or stresses than the original (ground subsidence, new constructions built in adhesion);
for water infiltration (rainwater, leaks from drains and pipes);
due to ageing of materials (mortar weakened by moisture and salts, oxidised keys and reinforcement rods, rotten wood);
for subsequent changes that may have affected the bonding of the masonry (new openings, renovations);
for possible cases of original inexperience in construction due to inadequate material
59-67

## Slide 46
  Learning Unit 6: IDismantling/demolition
62
Demolition order
Demolition work must proceed carefully and in an orderly manner, must be carried out under the supervision of a supervisor, and must be conducted in a manner that does not jeopardise the stability of the load-bearing or connecting structures and any adjacent structures.
The sequence of the work must be set out in a schedule, which must be kept available to all
59-67

## Slide 47
  https://biblus.acca.it/focus/piano-demolizioni/
  https://www.ediltecnico.it/59281/sicurezza-nelle-demolizioni-normativa-tecniche-azioni/
  https://www.manomano.it/consigli/tetto-verde-guida-completa-8285
  Innovazione e valorizzazione Efficienza Energetica: PROGETTO INNOVA PALERMO
  UNI 11235, “Istruzioni per la progettazione, l’esecuzione, il controllo e la manutenzione di coperture a verde”, 2007.
  Francesca Salvo, Patrizia Piro, Gennaro Nigro, Manuela De Ruggiero, Modello economico di stima dei tetti verdi negli edifici residenziali, rivista valori e valutazionin. 88 18 - 2017
  Raul Berto, Giovanni Cechet, Carlo Antonio Stival, Le prestazioni connotanti delle coperture verdi cap. 3
  Raul Berto Giovanni, Cechet Paolo, Rosato Carlo Antonio, Stivai Edino Valcovich, Le coperture verdi: Implicazioni tecnologiche, strutturali, energetiche ed economico - sociali
  ANIT, Prestazioni energetiche dei tetti verdi, Settembre 2020
  ZinCo, Sistemi per tetti verdi
References
Journals and Publications
68