## Slide 1
Module 2:
Sustainable roofing methods
Funded by the European Union. Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Education and Culture Executive Agency (EACEA). Neither the European Union nor EACEA can be held responsible for them.
Open licence: This document is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International licence.

## Slide 2
Presentation Flow
  TOPICS DISCUSSED
  Introduction to green roof systems and environmental benefits
  Green roof energy savings in buildings
  Green roofs as a nature-based solution in urban areas
  Green roof waterproofing, drainage & recovery
  Integration of renewable systems in green roofs
02

## Slide 3
03
  Introduction
This module covers the benefits of green roofs in economic, energy and environmental terms. It also introduces topics such as efficient water management or the introduction of renewable technologies on green roofs.
Understanding the impact of green roofing on building energy savings is one of the main objectives of this module.

## Slide 4
  Learning Unit 1: Introduction to green roof systems and environmental benefits

## Slide 5
PURPOSE OF GREEN ROOFS
  Learning Unit 1: Introduction to green roof systems and environmental benefits
Green Roofs represent sustainable urban planning with a multitude of benefits, both for the building and the urban environment.
Sustainable urban development aims to minimise damage to the environment while preserving as much of our resources as possible and transitioning to renewable resources wherever possible.
Currently, green roofs are considered a cost-effective strategy for creating more livable and sustainable cities.
A green roof is a constructive installation that has a vegetation cover on top of soil or substrate and is specially conceived to obtain environmental benefits.
The roof contains four main components: a membrane to protect the structure of the roof, a drainage layer, growing medium and finally the vegetation.
Urban implications
What is a green roof?

## Slide 6
GREEN ROOF SYSTEMS
  Learning Unit 1: Introduction to green roof systems and environmental benefits
Roof garden with permanent irrigation and deep soils, suitable for lawns, shrubs, and trees, and walkways (highest maintenance).
This type of green roof implies great environmental benefits (biodiversity, reduction of the heat island effect, improvement of air quality, etc.) but also other social benefits due to its accessibility (creation of vegetable gardens, better comfort of residents and quality of life, etc.).
Intensive green roofs
Green roofs can also be categorized into different types:
EWHA Womans University.
Dominique Perrault architecture Seoul, South Korea Credit: André Morin / DPA / Adagp
Suitable for visible and accessible roofs, they require green and flowering plants throughout the year.
Semi or simple-intensive
Green protection layer for roofs with little load-bearing capacity. Shallow soil suitable for less demanding plants (low maintenance).
The benefits of this type of green roof are environmental (water management, reduction of the heat island effect, reduction of the building's energy consumption, etc.) but can also benefit the building in which it is located (lower energy costs, lower maintenance costs, etc.).
Extensive green roofs
California Academy of the Sciences.
Renzo Piano Building Workshop San Francisco, California, United States Credit: Tom Fox, SWA Group

## Slide 7
GREEN ROOF SYSTEMS
  Learning Unit 1: Introduction to green roof systems and environmental benefits
Extensive green roof
Semi-Intensive green roof
Intensive green roof
TYPES
Of green roofs

## Slide 8
GREEN ROOF SYSTEMS
  Learning Unit 1: Introduction to green roof systems and environmental benefits
The above systems also differ in the layers of materials of which they are composed. These layers have an impact on the effects produced by the green roof.
Sedum succulents
Substrate
Protection layer
Waterproof membrane
Separation layer
Insulation
Roof Deck
Sedum/ Native Grasses
Substrate
Filter fabric
Drainage layer
Protection layer
Waterproof membrane
Separation layer
Insulation
Roof Deck
Diverse plantings
Substrate
Filter fabric
Drainage layer
Protection layer
Waterproof membrane
Separation layer
Insulation
Roof Deck

## Slide 9
IMPROVEMENT PARAMETERS
  Learning Unit 1: Introduction to green roof systems and environmental benefits
The integration of green roofs into the urban landscape can bring certain environmental, but also economic and social benefits. This implies that green roofs can improve certain parameters classified as follows:
Improvement of air quality
Improvement of stormwater management
Reduction of energy consumption
Reduction of the urban heat island effect
Promotes biodiversity
Environmental
Appreciation of the land value
Employment enhacement
Reduction of energy consumption
Extends life span of roof
Economic development
Economic
Reduction of ambient noise
Improvement of the aesthetics of a building
Generation of a greater sense of well-being
Social

## Slide 10
KEY POINTS
  Understand the basic concepts of green roofs.
  Understand the different types of green roofs and the benefits they offer to the urban area.
  Be aware of the importance of the presence of green spaces in cities and its urban implications.
  Determine the environmental parameters for improvement with green roofs.
  Identify the parameters for the improvement of urban areas influenced by green roofs (environmental, economic and social).
  Learning Unit 1: Introduction to green roof systems and environmental benefits

## Slide 11
  Learning Unit 2: Green roof energy savings in buildings

## Slide 12
ENERGY BENEFITS OF GREEN ROOFS
  Learning Unit 2: Green roof energy savings in buildings
Green roofs are able to improve the energy efficiency of a building and reduce its energy consumption through various phenomena.
Vegetation properties
The first phenomena is due to different characteristics of plants, such as their consumption of sunlight energy due to the performance of different physiological processes such as photosynthesis and evapotranspiration, as well as the generation of shadows on our roof and the reflectivity of the plants.
PHENOMENA FOR ENERGY SAVING IN BUILDINGS
b. Thermal insulation
Improving the thermal insulation of the building is the main purpose of the green roof. In other words, means to decrease the thermal transmittance of the roof.
c. Thermal mass
Directly dependent on the mass of the different layers especially the substrate and vegetation, and the specific heat of each layer. A high thermal mass helps to stabilise building temperatures, thus reducing peak demand.

## Slide 13
PHENOMENA FOR ENERGY SAVING IN BUILDINGS
  Learning Unit 2: Green roof energy savings in buildings
Vegetation properties
1. The consumption of solar energy by the vegetation
This effect results in a decrease of the temperature inside the building, especially on the floors closest to the roof.
It mainly depends on the following vegetation phenomena:
2. Process of evapotranspiration
Evapotranspiration is the combination of two processes:
- Evaporation from the soil and from the surface covered by plants.
- Transpiration from plant leaves.
This phenomenon also causes green roofs cool down through latent heat loss, lowering the temperature of the air above the roof and the temperature of the substrate.
3. Reflection of light on an exposed surface
Green roofs are therefore cooled by enhancing the reflectivity of incident solar radiation.

## Slide 14
  Learning Unit 2: Green roof energy savings in buildings
b. Thermal insulation
PHENOMENA FOR ENERGY SAVING IN BUILDINGS
To understand the effect of insulation on energy savings, it is important to understand the different layers that make up a green roof.
Of these layers, the ones that have the greatest effect on the thermal insulation of the roof are:
Reminder of the layers of a green roof
Thermal insulation.
Waterproof membrane.
Drainage or water storage material.
Filter layer.
Root barrier.
Substrate.
Vegetation.
The insulation layer
The drainage or water storage system
The substrate. The substrate can vary the transmittance of the roof depending on two factors, the bulk density of the soil and its humidity content.
A low bulk density leads to a high thermal diffusivity which results in a low thermal transmittance.
A high percentage of humidity increases the thermal transmittance of the floor.

## Slide 15
  Learning Unit 2: Green roof energy savings in buildings
PHENOMENA FOR ENERGY SAVING IN BUILDINGS
b. Thermal insulation
To calculate the energy savings due to thermal insulation, the parameters that mainly influence are:
Heat transfer Q
Thermal transmittance U
Convective heat transfer coefficient h
Thermal conductivity K
Thermal diffusivity α
Conduction is the transfer of heat between substances that are in direct contact with each other. Convection is the heat transfer by the macroscopic movement of a fluid.
Physical property of materials that measures the amount of energy an element passes through in a unit of time.
Heat transfer rate between a solid surface and a fluid per unit area per unit temperature difference. It depends on the physical properties of the fluid and the physical situation.
Ability to transmit heat measured through the magnitude known as thermal conductivity coefficient.
It is the rate at which heat diffuses through a material, so the higher the conductivity, the higher the diffusivity.

## Slide 16
  Learning Unit 2: Green roof energy savings in buildings
PHENOMENA FOR ENERGY SAVING IN BUILDINGS
b. Thermal insulation
The following formulas regulate the behaviour of the green roof for heat transfer:
The heat transfer (W) through the walls, it can be expressed with "Fourier's Law“:
eat transfer area (
dT = = temperature gradient - difference over the material (°C, °F)
Q=U·A·dT
Heat transfer coefficient per unit area or transmittance
material thickness
convective heat transfer coefficient
Thermal conductivity of the material

## Slide 17
  Learning Unit 2: Green roof energy savings in buildings
ENERGY SAVING ON GREEN ROOFS
Green roofs can be considered as passive elements.
Passive measures are based on the model of sustainable architecture using environmentally friendly techniques and materials, incorporating as much as possible the conditions of the environment and minimising the negative impact of the building.
Green roof helps regulate the temperature of the roof and the interior of the building, thereby reducing the amount of energy used for cooling and, therefore, the associated costs.
Total energy savings vary greatly depending on roof design, climate and building height.
The highest energy saving potential corresponds to those cases where the green roof is installed on poorly insulated buildings.
These savings are around 1-15% of annual energy consumption due to reduced use of cooling and heating systems and milder indoor temperatures.

## Slide 18
KEY POINTS
  Introduce and understand the different phenomena for energy savings that occur on a green roof.
  Analyse the impact of the green roof on the energy savings of a building.
  To know the parameters and formulas that characterize the energy insulation phenomena produced by a green roof.
  Understand the heat transfer behaviour.
  Ultimately, understand that when installed on the roof of a building, modify the energy transfer between the roof of the building and the exterior, increasing the albedo of the roof, increasing the thermal inertia of the roof and attenuating the temperature values supported by the roof of the building.
  Learning Unit 2: Green roof energy savings in buildings

## Slide 19
  Learning Unit 3: Green roofs as a nature-based solution in urban areas

## Slide 20
GREEN ROOFS AS A NATURE-BASED SOLUTION IN URBAN AREAS
  Learning Unit 3: Green roofs as a nature-based solution in urban areas
What is a nature-based solution?
The International Union for Conservation of Nature (IUCN) defines nature-based solutions (also referred to as NBS) as “actions to protect, sustainably manage and restore natural and modified ecosystems in ways that address societal challenges effectively and adaptively, to provide both human well-being and biodiversity benefits.
Why green roofs are a nature-based solution?
Green roofs are a technology that can help mitigate some of the negative effects of hard urban landscaping by reintroducing a natural landscape into urban city environments.
In addition, they can bring numerous social, environmental and economic benefits to an urban area.

## Slide 21
  Learning Unit 3: Green roofs as a nature-based solution in urban areas
BENEFITS OF GREEN ROOFS
Biodiversity and habitat improvement
Green roofs can provide new habitats for plants and animals in urban areas, increasing local biodiversity.
Its contributes to the ecologycal balance of the city, preventing pets and protecting and feeding other animal species like birds or differents types of pollinators.
Stormwater management
Green roofs are one of the best solutions to the storm water in cities, they are able to address wet weather flows, reduce the rate of runoff by 65%, extend the amount of time it takes for water to leave a site by up to 3 hours and they also can protect cities from acid rain.
Rainwater can be as well captured and used for irrigation, flushing toilets, and for other non-potable purposes.

## Slide 22
  Learning Unit 3: Green roofs as a nature-based solution in urban areas
Urban Heat Island (UHI) effect
This effect is common in cities where natural landscapes have been replaced with non-reflective surfaces that absorb most of the solar radiation and re-radiate back into the environment as heat. Heat islands increase energy consumption and can cause heat-related illness.
Energy consumption of buildings
Green roofs can reduce the amount of heating from solar radiation a building experiences in the summer, and can insulate buildings
Air quality and fire barrier
Green roof can be a net carbon sink and can also absorb air pollutants and particulate and can also act as a fire barrier.
BENEFITS OF GREEN ROOFS

## Slide 23
  Learning Unit 3: Green roofs as a nature-based solution in urban areas
Urban Agriculture.
Green roofs could offer an outlet to educate urban residents about food and may boost local gardening efforts and generate jobs.
Acoustic Isolation.
Green roofs reduce noise better than traditional and concrete roofs. The effect is especially pronounced in densely populated areas where outside noise is greater.
Aesthetics and quality of life.
Green roofs create an attractive space, reducing stress and improving worker productivity
BENEFITS OF GREEN ROOFS

## Slide 24
  Learning Unit 3: Green roofs as a nature-based solution in urban areas
Economics benefits
Green roofs can provide green job generation through the production, installation and maintenance of green roofs and it also can provide investment benefits for building developers and owners and provide marketing opportunities to the building. In addition, green roofs increase the life span of buildings.
BENEFITS OF GREEN ROOFS

## Slide 25
  Learning Unit 3: Green roofs as a nature-based solution in urban areas
Various tools are available to model and simulate the effects of green roofs among them are Canopy models coupled to building energy models (CM-BEM), Software ENVI-met and Trnsys.
TOOLS
For modeling the effect of green roofs in urban areas

## Slide 26
KEY POINTS
  What is a nature-based solution?
  Understand how green roofs affects wildlife in cities.
  Know how this technology is able to manage waterstorm.
  Energy savings of this technique.
  The effects of green roofs in the micro-weather and micro-economy.
  Green roof as an acoustic and fire barrier.
  Economic benefits.
  Tools to study green roofs.
  Learning Unit 3: Green roofs as a nature-based solution in urban areas

## Slide 27
  Learning Unit 4: Green roof waterproofing, drainage & recovery

## Slide 28
CURRENT PROBLEMS AND BACKGROUND
  Learning Unit 4: Green roof waterproofing, drainage & recovery
The development of cities has meant that natural ground cover has been replaced by artificial surfaces such as asphalt and concrete, which prevent rainwater from being absorbed by the ground.
This excess rainfall runoff can cause numerous environmental problems such as:
- Damaging water quality by carrying urban pollutants into water bodies
- Eroding riverbanks
- Flooding
Especially in high-density urban areas, green roofs can be the most practical way to deal with sewer overflows.

## Slide 29
STORMWATER MANAGEMENT ON GREEN ROOFS
  Learning Unit 4: Green roof waterproofing, drainage & recovery
In these systems, the growing medium covers a separate drainage layer that is usually sand or gravel or covered with a filter fabric, or a layer of synthetic geocomposite of plastic, rigid filaments, or the like.
Multi-layer systems
Such as sand and gravel, tend to increase retention time and delay peak runoff.
Granular drainage layers
  Reducing runoff
Green roofs help regulate stormwater and mitigate the effects of pollutant rainfall such as acid rain, mainly with two actions:
Increasing the amount of water that remains in the cover after a storm.
Reducing the rate at which water flows from the roof to the storm drain.
The ability of a green roof to absorb and retain rainwater depends on several factors, including the drainage layer, the growing medium, the plants (or vegetation), the slope of the roof, the season and climate and the roof size.
Choosing plants with higher evapotranspiration rates increases the rainwater absorption of a vegetative cover.
Drainage systems
Depth of the substrate

## Slide 30
STORMWATER MANAGEMENT ON GREEN ROOFS
  Learning Unit 4: Green roof waterproofing, drainage & recovery
  b. Reducing pollution
The buffering of the effects of acid rain
The filtration of various pollutants contained in the rain.
Green roofs can be a key element of a stormwater management plan, reducing peak flows by up to 65% and increasing the time it takes for water to flow from one location to the sewer by up to three hours.
Plants are able to absorb and incorporate into their tissues various polluting substances as well as acting as a protective layer against the buildings where they are located.
Particular attention should be paid to the nutrients supplied to the plants (phosphorus and nitrates), as the fertilizers used can be washed away by rainfall and contaminate nearby water bodies.

## Slide 31
RAINWATER RECOVERY SYSTEM
  Learning Unit 4: Green roof waterproofing, drainage & recovery
There are rainwater harvesting systems on green roofs, which collect all the water that is not consumed by the plants and guide it to a tank or cistern. This rainwater harvesting system is capable of recovering and filtering up to 60% of the rainwater.
The rainwater harvesting system can be installed in all types of buildings (houses, factories or companies) to achieve a sustainable benefit (economic, social and environmental) and have a positive and cyclical impact on the culture of environmental care.
Some systems, such as the one shown below, have a pump to direct the water to the roof. The water is recirculated back to the roof to be used for irrigation of vegetation.
Green roof
Runoff/Percolation
Watering
Building
Rainwater cistern
General rainwater network

## Slide 32
KEY POINTS
  Green roofs are a nature-based solution that can help regulate stormwater and mitigate the effects of polluting rainfall.
  Green roofs can be a key element of a stormwater management plan to deal with sewer overflows.
  Drainage systems as well as other factors act to reduce runoff.
  There are different systems that help to recover rainwater and reuse it as a sustainable practice.
  Learning Unit 4: Green roof waterproofing, drainage & recovery

## Slide 33
  Learning Unit 5: Integration of renewable systems in green roofs

## Slide 34
  Learning Unit 5: Integration of renewable systems in green roofs
RENEWABLE SYSTEMS IN GREEN ROOFS
The combination of renewable energy generation with green roofs has a lot of potential because not only achieves the benefits of each individual measure, but they are also positively related and enhance each other.
Conventional Green roofs
PV panels
Wind turbine
Biomass
Renewable systems
Increases the value of the green roof.
Generates more benefits for the green roof and the user.

## Slide 35
  Learning Unit 5: Integration of renewable systems in green roofs
BENEFITS OF RENEWABLE SYSTEMS IN GREEN ROOFS
On-site generation of renewable energy, which can also be used to power irrigation equipment for the green roof.
Increased revenue/savings (from generated energy) can offset the additional costs of a green roof.
Better use of space that captures the benefits of both technologies.
Using vertical axis wind turbines at edges and corners of green roofs could take advantage of turbulent wind without regard to orientation, while also reducing wind uplift forces and allowing for a more moderate rooftop microclimate.
Wind Energy details
- Produces green energy
Non-polluting
Reduces the use of fossil fuels
Inexhaustible
Wind energy
Wind energy benefits on green roofs

## Slide 36
  Learning Unit 5: Integration of renewable systems in green roofs
Biomass
The residual biomass of green roof or wall plants can be harvested to generate energy.
If biomass production is a goal, plants that produce more biomass than typical green roof plants can be selected if water, nutrients, and structural loading capacity are available.
Some of the ideal species for the incorporation of biomass in vegetative covers are herbaceous plants such as carinata or rapeseed, which are fast-growing.
Biomass Energy details
- Reduced dependence on fossil fuels
Renewable and very abundant source of energy
Cleaning of forests
Affordable price
Biomass energy benefits on green roofs
BENEFITS OF RENEWABLE SYSTEMS IN GREEN ROOFS

## Slide 37
  Learning Unit 5: Integration of renewable systems in green roofs
On-site generation of renewable energy, which can also be used to power irrigation equipment for the green roof.
Increased revenue/savings (from generated energy) can offset the additional costs of a green roof.
Solar PV panels protect the plants and growing media from direct exposure to sunlight and wind, reducing drying and excessive evapotranspiration, which enhances plant growth and creates microhabitats that encourages species variety.
Racking and support systems for solar PV panels can be designed so that the green roof layers act as tiles, thereby saving the need for roof penetrations or concrete pavers.
Increased membrane life due to the protection of green roofs mean solar PV panels must be moved for re-roofing less often.
Better use of space that captures the benefits of both technologies.
Increased efficiency of solar PV panels due to reduced ambient temperature from evapotranspiration.
BENEFITS OF RENEWABLE SYSTEMS IN GREEN ROOFS
Solar energy
Solar energy benefits on green roofs
Solar Energy details
Produces green energy
Low greenhouse gas emissions
Renewable and very abundant source of energy
Low maintenance.

## Slide 38
  Learning Unit 5: Integration of renewable systems in green roofs
To obtain the optimum values for the layout of the solar panels, different options can be selected to obtain the optimum tilt and azimuth. To do this, you must select:
Inclination: the inclination of the panels with respect to the horizontal plane must be entered.
Azimuth (orientation): This is the deviation, in degrees, from south. That is, -90º would be East orientation, 0º would be South orientation, and 90º would be West orientation.
SOLAR PANEL ORIENTATION IN A GREEN ROOF
Using the free online PVGIS software, the photovoltaic energy produced by any photovoltaic installation in Europe can be calculated.
This software allows three different types of installations: grid-connected PV systems, tracking PV and off-grid PV systems.

## Slide 39
  Learning Unit 5: Integration of renewable systems in green roofs
RESEARCH ON PV PANELS ON GREEN ROOFS
Did you know that...?
A comparison of two solar-clad roofs in Sydney, Australia, one bare under its panels and the other adorned with native grasses and plants, has revealed that the green roof panels were, on average, 3.63% more efficient, producing a 13% higher daily average than the conventional roof.
  Click on the book to read more
  Solar PV panels are less efficient as ambient temperatures rise. High rooftop temperatures increase the conductivity of a crystalline silicon panel’s semiconductor, which in turn inhibits charge separation and lowers the voltage of the solar cell (Peck and van der Linde, 2010). Solar PV panels are 0.4-0.5% less efficient per 1 ̊C (1.8 ̊F) increase in ambient temperature, above 25 ̊C (77 ̊F).
  Click on the book to read more
  Jahanfar et al. (2020) created an evapotranspiration model for solar PV-integrated green roofs, finding that shading and wind-shielding from solar PV panels directly block solar radiation onto the underlying plants, reducing evapotranspiration rates and by ex-tension, water use.
  Click on the book to read more

## Slide 40
KEY POINTS
  Learning Unit 5: Integration of renewable systems in green roofs
  The combination of green roofs with different renewable energies is not only possible but also extremely beneficial because they enhance each other.
  How green roofs are enhanced with wind generation.
  How interacts the production of biomass with the green roof.
  Benefits of the PV generation integrated in green roofs.
  PVGIS as a tool for calculate photovoltaic systems.

## Slide 41
  Greater London Authority. (2008). Living Roofs and Walls - Technical Report: Supporting London Plan Policy. London: Design for London.
  Administration, G. S. (2011). The Benefits and Challenges of Green Roofs on Public and Commercial Buildings. United States.
  Bergman, T. L., Lavine, A. S., Incropera, F. P., & Sons, J. W. (2011). Fundamentals of Heat and Mass Transfer. ISBN: 978111813725.
  Castleton, H., Stovin, V., Beck, S., & Davison, J. (2010). Green roofs - building energy savings and the potential for retrofit. Energy and Buildings, 1582-1591.
  Chemisana, D., & Lamnatou, C. (2014). Photovoltaic-green roofs: An experimental evaluation of system performance. Applied Energy, 246-256.
  E. Jamei, H. C. (2023). Green roof and energy – role of climate and design elements in hot and temperate climates. Heliyon.
  ENVI-met. (n.d.). Climate change adaptation and environmental modeling. Retrieved from https://www.envi-met.com/es/software/
  Grow Green Project - H2020. (2020). Compendium of Nature-based and ‘grey’ solutions to address climate- and water-related problems in European cities.
  Hirano, Y., Ihara, T., Gomi, K., & Fujita, T. (2019). Simulation-Based Evaluation of the Effect of Green Roofs in Office Building Districts on Mitigating the Urban Heat Island Effect and Reducing CO2 Emissions. Sustainability.
  Hui, S. C., & Chan, S. (2011). Integration of green roof and solar photovoltaic systems.
  Lamnatou, C., & Chemisana, D. (2015). A critical analysis of factors affecting photovoltaic-green roof performance. Renewable and Sustainable Energy Reviews, 264 - 280.
  Natural Watre Retention Measures. (n.d.). Green Roofs. Retrieved from http://nwrm.eu/
  Niachou, A., Papakonstantinou, K., Santamouris, M., Tsangrassoulis, A., & G. Mihalakakou. (2001). Analysis of the green roof thermal properties and investigation of its energy performance. Energy and Buildings, 719-729.
  UTS - University of Technology Sydney. (2021). Green Roof & Solar Array – Comparative Research Project.
References
  Module 2:
  Sustainable roofing methods
  REAL ESTATE LISTING － JANUARY 2020