## Slide 1
Module 5: HEALTH & SAFETY PRACTICES
Funded by the European Union. Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Education and Culture Executive Agency (EACEA). Neither the European Union nor EACEA can be held responsible for them.

## Slide 2
  Learning Unit 1: Occupational health & safety standards
02

## Slide 3
Working / walking on roofs
Design Specifications
  Walking or working on roofs is not permitted without a special permit.
    In order to walk on the roof (visits, inspections,...etc.), personnel must be trained and the route to be followed must have been defined, secured and protected
    In order to carry out work on roofs, it is necessary to follow the procedure defined by current regulations
  All entrances to the roof must be closed with a no-entry sign.
  Learning Unit 1: Occupational health & safety standards
03
02-05

## Slide 4
Working / walking on roofs
Design Specifications
  Walking/working on the roof must take place safely;
    Firstly, collective protection systems must be used to prevent roof collapses (complete floors resting on beams) and falls due to the risks inherent in the elevated position (protective barriers, footbridges, handrails, manhole covers).
    If this is not possible, safety nets can be used under the roof (collapse) or on the end of the roof (fall from a high position).
    If this is not possible, lifts or suspended baskets by means of cranes may be used. In these two cases, personnel are required to wear fall protection equipment and, in the second case (basket), a lifting plan must be drawn up.
    If this is not possible, personnel must be equipped with suitable fall protection devices (approved full body harness, energy-absorbing lanyard if the fall potential is more than 4 metres) or short restraint lanyard (if the fall potential is less than 4 metres), self-locking spring hooks (or karabiners) and secure anchorage points. Alternatively, a full body harness and fall arrest system can be used.
04
  Learning Unit 1: Occupational health & safety standards
02-05

## Slide 5
FALL FROM HEIGHT
event involving a risk of a person falling regardless of height
WORK AT HEIGHT
work activity that exposes the worker to the risk of falling from a height of more than 2 m above a stable surface.
05
  Learning Unit 1: Occupational health & safety standards
02-05
Notes:
In order to reduce the consequences of a fall, systems are used that prevent impact on the ground by slowing and stopping the falling movement and at the same time do not have to apply a force to the falling body,
a stopping force of more than 6kN (600kg)

## Slide 6
  Learning Unit 2: Safety and protection equipment
06

## Slide 7: In Work at Height, the risks are:
Suspension
impact
Fall
Pendulum effect
recovery
07
  Learning Unit 2: Safety and protection equipment
06-14

## Slide 8
Free fall: between 0.6 and 1.5 m
Limited free fall: max. 0.6 m
Contained fall
IMPEDITED Fall
08
  Learning Unit 2: Safety and protection equipment
06-14

## Slide 9
The fall factor
The fall factor (FF) is defined as the ratio between the free fall of a body and the length of the fixed lanyard connecting it to an anchorage point.
Let us therefore see how to determine the free fall space
09
  Learning Unit 2: Safety and protection equipment
06-14

## Slide 10
The FF has a value < of 1 when the anchorage point is located above the harness attachment ring (which is normally 130/150 cm from the walking surface)
L = Lanyard length
D = Height difference between sling attachment and point of anchor
C = L-D) fall < of L
Therefore FF< 1
10
  Learning Unit 2: Safety and protection equipment
06-14
Anchorage Point
Difference between heights D
harness attachment
Fall

## Slide 11
L = Lanyard length
D = Height difference between connection
harness and anchorage point (D = 0)
C = Fall (L-D = L) fall equal to length of lanyard
whence FF = 1
The FF has a value = to 1 when the anchor point is at the same height as the harness attachment ring
11
  Learning Unit 2: Safety and protection equipment
06-14
Anchorage Point
Difference between heights D=0
harness attachment
Fall= L

## Slide 12
Fall C = L+D so fall > L and the FF is > 1
The FF has a value > to 1 when the anchor point is below the point of the harness attachment ring
12
  Learning Unit 2: Safety and protection equipment
09-19
Anchorage Point
Difference between heights D
harness attachment
Fall = L+D
Lanyard length L

## Slide 13
Minimum safety distance required between the point of walking and the point of impact.
Starting distance (L lanyard - height 1)
Absorber elongation
Lanyard length
Operator space
Residual free space
Anchor line arrow
C = 1+2+6
C
13
  Learning Unit 2: Safety and protection equipment
06-14

## Slide 14: If we add 1 (one) metre tolerance to the drop space, we have defined the air gap!
111
14
  Learning Unit 2: Safety and protection equipment
06-14

## Slide 15
  Learning Unit 3: Pre- and post-operational checks
15

## Slide 16: Pendulum Effect
The pendulum effect, during a fall from height, is an uncontrolled rotation and oscillation movement from which a 'risk of violent impact' against lateral or ground obstacles arises.
16
  Learning Unit 3: Pre- and post-operational checks
15-23
Effect of lateral offset relative to the anchorage point
Legend
1 Height of the starting position
2 Height of the final position before activation of the fall arrest device

## Slide 17
17
  Learning Unit 3: Pre- and post-operational checks
15-23
Simple pendulum effect
oscillation of the body with impact against obstacles

## Slide 18: In order to eliminate the risk of falling, it is necessary to use fall-arrest systems with a second anchorage point to which an additional lanyard can be attached (fig. 1) or to use a fall-arrest rope deflection point (fig. 2). The USE prescriptions for the fall arrest system are provided by the client and must be adhered to.
18
  Learning Unit 3: Pre- and post-operational checks
15-23
DOUBLE ANCHORAGE POINT
POINT OF FALL DEFLECTION

## Slide 19: Why perform periodic checks?
All equipment, in particular safety equipment,
must be kept efficient and regularly inspected.
Failure to carry out periodic checks can lead to the ineffectiveness of the protection system and the lapse of liability on the part of the manufacturer.
In the event of an accident, if maintenance has not been carried out properly, the owner of the anchorage system (owner, building manager, employer, etc.) takes full responsibility.
127
19
  Learning Unit 3: Pre- and post-operational checks
15-23

## Slide 20: Lifeline control diagram *
End and intermediate elements: Check for deformations
Turnbuckles:
Check the cable tension Check the presence of the lead
Shock absorbers:
Check for deformations and
elongations
Always and for everything
  Check bolting tightness
  Check that the part has not been modified
  Check for corrosion
* To be provided by the manufacturer and specific to each type of anchorage.
20
  Learning Unit 3: Pre- and post-operational checks
15-23

## Slide 21
Clamps:
Check cable crimping
Cables:
Check cable tensioning Check cable diameter Check for deformation
Stakes:
Check that the part is not broken or deformed
Signpost:
Verify the presence of the sign Verify the date of the last verification
Structural anchorage (mechanical dowel, threaded rod, anchor screws) If possible, exert a minimum force of 5 kN (500 kg) directly on the anchors, otherwise on the posts, for 15 seconds, check by means of a dynamometer that the test value does not decrease.
21
  Learning Unit 3: Pre- and post-operational checks
15-23

## Slide 22
HOW TO WEAR A HARNESS
Grasping the harness
for the dorsal ring.
Shake it so that the
belts go to their
place
If the braces
and/or the belt of
positioning are
tied, loosen them and
untie them
Slide the
braces over the shoulders
so that the 'D' ring will
found in the centre of the
back between the shoulder blades
22
  Learning Unit 3: Pre- and post-operational checks
15-23

## Slide 23: HOW TO WEAR A HARNESS
Passing a thigh strap between the
legs and connect it to the other
ends. Repeat with
the other leg. In case of
harness with belt
close it and adjust it afterwards
adjusting the leg loops
Connect the belt
frontal positioning
in the centre of the chest.
Tighten to
ensure the correct
suspender trim
Carry out the
adjustment so that
the harness is well
adherent allowing
movement anyway.
23
  Learning Unit 3: Pre- and post-operational checks
15-23

## Slide 24
  Learning Unit 4: First aid techniques
24

## Slide 25
RESCUE THE INJURED PERSON
In order to be effective, first aid action must guarantee the best and quickest conditions for intervention and, when necessary, for transporting the injured person to the place where appropriate treatment will be administered.
In the most trivial and simple to manage cases (e.g. abrasions and/or cuts), the 'first aider' will be able to give advice by providing the first-aid pack or box, as well as applying minor dressings if necessary; in more serious cases, he/she will try to stabilise the injured person while waiting for help to arrive.
Act with calmness and determination.
  Learning Unit 4: First aid techniques
25
24-45

## Slide 26
Awaiting rescue will have to:
maintain a calm attitude;
carry out only those interventions that are strictly necessary;
assess the person's condition (the nature and extent of the discomfort): with particular reference to vital functions: consciousness (awareness of self and surroundings), breathing and any bleeding in progress, (always assess the possibility of any fractures in case of trauma, with particular attention to vertebral fracture in case of falls);
reassure the casualty; if possible explaining what you are doing, and if possible ask him/her about useful rescue information (e.g. what happened, does he/she have a heart condition, where does he/she feel pain, is he/she diabetic, did he/she hit his/her back or head, does he/she feel like vomiting) do not comment on the incident with the casualty about the injuries and their severity;
26
24-45
  Learning Unit 4: First aid techniques

## Slide 27
do not move the injured person except in cases of imminent danger, do not stand or sit, avoid moving or lifting a traumatised person;
refrain from administering any type of medication, drink or food;
do not perform medical manoeuvres (e.g. reduction of fractures or dislocations, extraction of foreign objects from any part of the body);
if the casualty is unconscious, carry out the first necessary measures within the limits of one's own competence, including assessment and support of vital functions;
do not abandon the injured person.
27
24-45
  Learning Unit 4: First aid techniques

## Slide 28
SPINAL COLUMN INJURIES
A spinal cord injury can involve only the bony structure or it can affect the spinal cord contained within the spinal canal.
Suspect this lesion if:
the injured person complains of back pain;
if they complain of tingling, electric shocks, a feeling of heat or cold in their extremities;
if he fell from a height, or standing from a height of more than 2 metres;
if he suffered head and/or facial trauma above the collarbone.
The absence of pain does not exclude that there may be a spinal injury.
28
24-45
  Learning Unit 4: First aid techniques

## Slide 29
WHAT TO DO
The rescuer must first check and safeguard vital functions and avoid handling the casualty.
Call for help promptly;
do not move the injured person;
Try to keep the patient's head immobile in a neutral position;
control respiratory activity.
Even minimal movements of the injured person can be dangerous.
29
24-45
  Learning Unit 4: First aid techniques

## Slide 30
Only in the case of immediate danger, where it is indispensable to move the injured person, and if at least three or four people are present, the move can be carried out as follows:
the first rescuer grabs the head with one hand under the chin and the other under the nape of the neck, pulling the head along the axis of the body;
the second grabs the ankles and pulls them in opposite direction;
the others place their hands under the thighs, the pelvis, the kidneys and the shoulder blades;
all lift the injured person on command trying to move the head, neck and torso, keeping him in traction, and placing him on a rigid stretcher, even a makeshift one.
30
24-45
  Learning Unit 4: First aid techniques

## Slide 31
CRANAL TRAUMA
Head injury is defined as any event that has contributed to altering the anatomo-functional balance of both the skull and the brain.
31
24-45
  Learning Unit 4: First aid techniques

## Slide 32
Head trauma can cause various types of injuries such as contusions, scalp abrasions or swellings, wounds and, finally, fractures of the vault and skull base; internal injuries, ranging from contusion, concussion to cerebral haematoma.
It is always of particular significance and in severe forms, there may or may not be: loss of consciousness, jet vomiting (without nausea), dizziness, intense headaches, asymmetry of the pupils, scalp injuries, bleeding from the nose (epistaxis), mouth or ears (otorrhagia), paralysis of the limbs or one side of the body.
In the case of a severe head injury, the appearance of a trickle of blood (otorrhagia) from one or both ears is strongly indicative of a fracture of the skull base (petrous fracture).
32
24-45
  Learning Unit 4: First aid techniques

## Slide 33
WHAT TO DO
When rescuing a head injury victim, the state of consciousness and respiratory function must be immediately assessed.
Ascertain consciousness and normal breathing (beware of the risk of vomiting);
if there are no suspicions of spinal trauma or other complications, it is advisable to place the casualty in a safe position: supine if the patient is conscious, keep the head in a slightly elevated position;
in the case of nose, mouth and ear haemorrhage: do not block the escape of blood from the orifices; it should drain;
urgently call the emergency services 118/112;
monitor the patient while waiting for help.
33
24-45
  Learning Unit 4: First aid techniques

## Slide 34
ABDOMINAL TRAUMA
It is a trauma that can cause severe damage to internal organs in the abdomen, with possible internal bleeding difficult to detect by a first responder.
Signs of local abdominal trauma may be evidenced by skin lesions, wounds, haematomas, ecchymosis, spontaneous abdominal pain and on palpation.
Symptoms of internal bleeding may be evidenced by signs of shock, paleness and sweating.
34
24-45
  Learning Unit 4: First aid techniques

## Slide 35
WHAT TO DO
Traumatised persons experiencing pain in the abdomen should be stretched out; their vital functions, particularly cardiovascular function, should then be assessed, and this assessment should continue until medical follow-up.
Alerting Advanced Rescue;
in the case of an abdominal wound, cover it with sterile dressing material, in the case of bleeding from the abdominal wall, try a compressive dressing, which is useless in the case of externalised internal bleeding;
In the case of leakage of the intestines, one must absolutely not try to reposition them inside the abdominal cavity, but must cover the viscera with a cloth, as sterile as possible;
if an external object is embedded, it must be left in place and an attempt must be made to stabilise it for subsequent transport;
Position the casualty in dorsal decubitus with the head slightly raised and the lower limbs flexed;
cover the patient.
35
24-45
  Learning Unit 4: First aid techniques

## Slide 36
CHEST TRAUMA
Violent shocks or strong compressions of the rib cage can cause bone injuries associated or not with internal injuries.
They may suggest thoracic trauma:
head injuries and associated abdominal injuries;
asymmetry in the expansion of the rib cage.
Obvious wounds do not always occur.
36
24-45
  Learning Unit 4: First aid techniques

## Slide 37
An injured person with chest trauma usually manifests:
pain during deep breathing, or with coughing, or which increases with palpation of the chest;
laboured breathing, which is subjectively felt as 'hunger/need for air' (dyspnoea);
cyanosis or pallor of the skin, sweating, agitation, rapid pulse.
37
24-45
  Learning Unit 4: First aid techniques

## Slide 38
WHAT TO DO
In the traumatised person with chest pain, respiratory and cardiovascular function in particular must be assessed.
If the patient is stable, have the subject assume a semi-sitting position to facilitate the descent of the diaphragm and improve ventilation;
in the case of a foreign body penetrating the chest, leave the object in place;
cover the injured person;
monitor vital parameters;
alerting the emergency services 118/112.
38
24-45
  Learning Unit 4: First aid techniques

## Slide 39
HEAT STROKE / SUNSTROKE
Prolonged stay in overheated environments can cause different pathologies, which are grouped under the term 'heat-related diseases'.
Heatstroke and sunstroke consist of an excessive increase in body temperature caused by high ambient temperature and the hindered dispersion of heat from the body.
39
24-45
  Learning Unit 4: First aid techniques

## Slide 40
The main signs and symptoms are:
high body temperature (over 40°);
congested face and red complexion;
mental confusion, possible loss of consciousness, convulsions;
dry and very hot skin;
impaired breathing (rapid, laboured breathing) and rapid pulse;
occasional occurrence of nausea and vomiting.
40
24-45
  Learning Unit 4: First aid techniques

## Slide 41
WHAT TO DO
Control and possible support of vital functions with basic techniques;
call for help;
transport the injured person to a cool, ventilated area and in any case away from the source of heat;
Place the subject lying down with shoulders slightly raised;
41
24-45
  Learning Unit 4: First aid techniques

## Slide 42
undress it and cool the surface of the body:
- with fresh sponges;
- spraying or pouring water;
- wrapping it in wet towels or cloths on which to pour water;
- if available, placing ice (also synthetic) wrapped in a cloth, under the armpits, knees, groin, wrists, ankles.
Do not give alcohol or iced drinks.
42
24-45
  Learning Unit 4: First aid techniques

## Slide 43
HYPERTHERMIA (Hypothermia)
Hypothermia is due to the individual's stay in environments with intense and prolonged cold, and is favoured by head trauma and intoxication by alcohol, carbon monoxide, prolonged fasting, bone marrow damage, and metabolic damage.
It consists of lowering the body temperature below 34°, which exceeds the body's thermoregulatory capabilities.
Cerebral vasoconstriction is at the root of the disorders experienced by the subject, who shows tachycardia, physical and mental sluggishness, irritability, difficulty with vision and speech, sluggishness in reasoning to the point of torpor.
43
24-45
  Learning Unit 4: First aid techniques

## Slide 44
It presents the main symptoms such as:
initial chills, increased respiratory rate;
impaired speech and movements, disinterest in the situation, hypersomnia;
muscle rigidity;
alterations in consciousness to the point of coma.
44
24-45
  Learning Unit 4: First aid techniques

## Slide 45
Basic principles of rescue at the scene
Timeliness of intervention;
prevent the patient from cooling down further, protection from the wind:
- transport the subject to a dry, warm, but not excessively heated environment;
- remove clothing if wet or frostbitten, try to warm the patient with massage and warm, dry cloths, without approaching heat sources directly;
- give lukewarm-warm sugary drinks (absolutely no alcohol);
control and possible support of vital functions with basic techniques;
alerting the rescue services
45
24-45
  Learning Unit 4: First aid techniques

## Slide 46
  L. Cortis - Relazione dal titolo “Pianificazione e misure di sicurezza da adottare nelle attività in copertura”. Convegno nazionale “Sistema linea vita - Misure di prevenzione e protezione nei lavori in quota per la manutenzione delle coperture. Le diverse procedure Regionali” organizzato a Bologna nell’ambito di Ambiente Lavoro dal COE il 17 ottobre 2013.
  F.M. Fabiani - “I ponteggi come protezione collettiva in relazione ai lavori su coperture” pubblicato su “La sicurezza nei lavori sulle coperture - Sistemi di prevenzione e protezione contro la caduta dall’alto”, INAIL, 2015.
  L. Rossi - “Ancoraggi. Requisiti prestazionali e geometrici per la sicurezza in copertura” pubblicato su Tecnologie & Soluzioni n.2, New Business Media Srl, marzo-aprile 2014.
  L. Rossi - “Le misure preventive e protettive per gli interventi sulle coperture” pubblicato su Ambiente & Sicurezza n. 2, New Business Media Srl, 3 febbraio 2016.
  L. Rossi - “Sicurezza in copertura- Quali misure adottare” pubblicato su Ambiente & Sicurezza n.1, New Business Media Srl, gennaio 2017.
  Manuale di primo soccorso, kiker edizione
  AAVV. PHTLS Prehospital Trauma Life Support. Seventh edition. Edizione italiana a cura di Alberto Adduci. Elsevier, 2011.
  Ministero dell’interno. Dipartimento dei vigili del fuoco, del soccorso pubblico e
  della difesa civile. Tecniche di primo soccorso sanitario (TPSS). Manuale esecutore.
  2012 [consultato maggio 2018] URL: http://www.vigilfuoco.it/sitiComandi/GestioneSiti/downloadFile.asp?s=321&f=49086.
References
Journals and Publications
46